## Slide 1: SPS Main Circuits Simulator
3 R-C channels for SPS RB, RQF and RQD circuits
Ground plane for good noise immunity
LEMO connectors
Mechanical integration in LO3 and 866 1-C02
3 units to produce (LO3, 866 1-C02, Spare)
R
C

## Slide 2: SPS Main Circuits Simulator
 | R | C
RB | 1 MΩ | 1.9 µF
QF | 1 MΩ | 1.2 µF
QD | 1 MΩ | 1.2 µF
 | RB | RQF/RQD
LOAD.OHMS_SER | 3.4 | 1.6
LOAD.HENRYS | 6.4 | 1.93
Time Constant (s) | 1.882 | 1.206
Max Current | 6000 | 2200
Current for DCCT 10V | 6000 | 5000
Max Voltage | 25000 | 4000
Circuit does not simulate saturation of magnet
R-C values chosen to match time constant of unsaturated circuits: